## Slide 1: Advances in open-source software for 3D electromagnetics using SimPEG
L. Heagy1, J. Kuttai1, D. Cowan1, J. Capriotti1,2, S. Kang3, D. Fournier4, D. Oldenburg1
1University of British Columbia Geophysical Inversion Facility
2Colorado School of Mines
3Stanford Geophysics
4Mira Geoscience

## Slide 2: some background: UBC-GIF
GIF Fortran Codes & GIF Tools
slide from: Oldenburg, 2016: Looking back and moving forwards (BIRS)

## Slide 3: some background: UBC-GIF
By 2010’s…
most forward simulations “solved”
next generation of research in inversions
physical properties: anisotropy, high contrasts, magnetic permeability, IP in EM
experimenting with inversion methods: choice of norm, including physical property & geologic information
role of machine learning
…
Transition to open-source
goal: common framework for inversions in geophysics to serve researchers
In 2013… started SimPEG
S. Kang
L. Heagy
R. Cockett

## Slide 4
simulation and parameter estimation in geophysics
common framework for simulations & inversions
accelerate research: build upon others work
facilitate reproducibility of results
build & deploy in python
open-source

## Slide 5: what simpeg solves
Given
observations:
uncertainties:
ability to forward model:
Inverse problem: Find an Earth model that fits those data and a-priori information

## Slide 6: flow chart for the inverse problem
many components
iterative process to obtain solution
each component requires evaluation, adjustment by user
Fundamentals of Inversion – D. Oldenburg
Capturing knowledge in code – L. Heagy
http://www.mtnet.info/EMinars/EMinars.html

## Slide 7: electromagnetics: basic equations (quasi-static)
* Solve with sources and boundary conditions
Time
Frequency
Faraday’s Law
Ampere’s Law
Constitutive
Relationships
(non-dispersive)
No Magnetic Monopoles

## Slide 8: electromagnetics: frequency domain equations
Use constitutive relations, reduce to two equations, one field, one flux
Finite volume discretization (e.g. Haber, 2014; Cockett et al., 2016)

## Slide 9: Solving an FDEM problem
Mesh types:
Tensor
OcTree
Curvilinear
Tetrahedral
J. Capriotti

## Slide 10
modules:
frequency domain
natural sources
time domain
physical properties:
supports anisotropic conductivity
variable magnetic permeability
IP parameters (1D fdem, tdem)
multiple formulations: E-B or H-J

## Slide 13: example: 3D simulation & inversion
model:
conductive L-block (1 Ωm)
half-space (100 Ωm)
survey:
natural source EM
frequencies: 10, 50, 200Hz
data: ZTEM

## Slide 14: simulation
model:
conductive L-block (1 Ωm)
half-space (100 Ωm)
survey:
natural source EM
frequencies: 10, 50, 200Hz
data: ZTEM
simulation:
OcTree mesh
run SimPEG & UBC E3DMT

## Slide 15: inversion
data
2028 data
uncertainties:
  5% relative error
  floor: 0.01 for 10 Hz, 50 Hz data, 0.005 for 200 Hz data
regularization
L2 smooth model
identical beta-cooling schedule

## Slide 16: inversion
SimPEG
7 iterations
final χ-factor of 0.47
parallelized with Python multiprocessing
runtime: 15 minutes
UBC E3DMT
8 iterations
final χ-factor of 0.55
parallelized with MPI
runtime: 11 minutes

## Slide 17: code validations
simpeg.xyz/validations
compare analytic, UBC Fortran, SimPEG
fdem dipole:
z=5m
separation: 10m
D. Cowan

## Slide 18: example: AEM inversion with sparse norms
seawater intrusion: TDEM over Salinas Valley in 2017, 2019
spatially constrained 1D inversions
introduce time-constraint
L0 in space & time
Kang & Knight, 2022; Kang BCGS talk 2022
2017
difference.
no time constraint
difference.
L2 time constraint
difference.
L0 time constraint
2017
2019
S. Kang
lateral
vertical
time

## Slide 19: electromagnetics: advanced capabilities
Parallelization via domain decomposition
Sparse / compact norms
Parametric inversions
Petrophysically & Geologically Guided Inversion (PGI)
Joint inversions
  same physical property
  cross gradient, joint total variation, PGI
(Oldenburg et al, 2020)

## Slide 20: now and the future
where we are…
1D inversions: spatial constraints, sparse norms
3D inversions: fdem & nsem comparable to UBC fortran, tdem still some efficiency improvements
joint inversions: cross-gradient, joint total variation, PGI
where we are going…
tutorials, efficiency, simplifying code
lots of research!
model
research drives development
partnerships with industry
MIT license: use, adapt, commercialize
PGI inversion
Individual inversions
serpentinized
density
susceptibility
locating serpentinized rock: quasi-geology model from multiple geophysical data sets

## Slide 21: getting connected
docs: docs.simpeg.xyz
newsletter: newsletter.simpeg.xyz
slack group: slack.simpeg.xyz

## Slide 22: thank you! … and join us at 3DEM-7
email: lheagy@eoas.ubc.ca
slides: bit.ly/heagy-2023-aem
This work is licensed under a Creative Commons Attribution 4.0 International License.
https://3dem-7.geosci.xyz